Assignment 2
Artificial Neural Networks

---
Team Members
- Nehal Bhagat, 110050008
- Tanmay Randhavane, 110050010
- Alok Yadav, 110050043
- Rajlaxmi, 110050087

---
Error Rate vs Number of Iterations

---
XOR
The plot of error rate vs number of iterations for varying learning rate while keeping the momentum factor constant (0.1).

---
XOR
The plot of error rate vs number of iterations for varying momentum factor while keeping the learning rate constant (0.1).

---
Palindrome
The plot of error rate vs number of iterations for varying learning rate while keeping the momentum factor constant (0.1).

---
Palindrome
The plot of error rate vs number of iterations for varying momentum factor while keeping the learning rate constant (0.1).

---
The Effect of Learning Rate

---
- As the learning rate increases the number of epochs (iterations) needed for the convergence decrease as can be seen in the following plots.
- For these experiments, we varied learning rate and kept momentum factor constant at 0.8.

---
Majority

---
Palindrome

---
XOR

---
Digit Recognizer

---
The Effect of Momentum Factor

---
- The number of epochs are generally less for momentum factor closer to 0.5. For momentum factors close to either 1 or 0 the number of epochs increase.
- For these experiments, we varied momentum factor and kept learning rate constant at 0.9.

---
Majority

---
Palindrome

---
XOR

---
Digit Recognizer

---
Effect of Symmetric Initialization

---
XOR

---
If all weights are initialized with same values, the error remains constant. This happens because, the backpropagation algorithm keeps on adding equal amount gradient (∆w) into each weight and thus the weights remain equal throughout the iterations, giving the same value of error.

---
Function of Hidden Layers

---
XOR
For learning rate = 0.6.
The hidden layer contains two neurons.
For the first neuron, the weights are (-1.73, 3.88, -3.65)
And its truth table is as follows, which corresponds to the rule,
(a+b')
Input 1	Input 2	Output
0	0	1
0	1	0
1	0	1
1	1	1

---
For the second neuron, the weights are (2.81, 4.69, -4.81).
And its truth table is as follows, which corresponds to the rule,
ab'
Input 1	Input 2	Output
0	0	0
0	1	0
1	0	1
1	1	0

---
The output layer contains one neurons.
For this neuron, the weights are (-2.2, -5.07, 5.61)
And its truth table is as follows, which corresponds to the rule,
(a'+b)
Input 1	Input 2	Output
0	0	1
0	1	1
1	0	0
1	1	1

---
Conclusion:
The output of XOR is calculated as follows:
Output = (a + b' )' + (ab')' = XOR(a, b)
Whose truth table is as follows:
Input 1	Input 2	Output
0	0	0
0	1	1
1	0	1
1	1	0

---
For learning rate = 0.1.
The hidden layer contains two neurons.
For the first neuron, the weights are (4.26, 2.84, 2.84)
And its truth table is as follows, which corresponds to the rule,
ab
Input 1	Input 2	Output
0	0	0
0	1	0
1	0	0
1	1	1

---
For the second neuron, the weights are ( 1.83, 5.21, 5.23).
And its truth table is as follows, which corresponds to the rule,
a+b
Input 1	Input 2	Output
0	0	0
0	1	1
1	0	1
1	1	1

---
The output layer contains one neurons.
For this neuron, the weights are (2.67, -6.00, 5.86)
And its truth table is as follows, which corresponds to the rule,
a'b
Input 1	Input 2	Output
0	0	0
0	1	1
1	0	0
1	1	0

---
Conclusion:
The output of XOR is calculated as follows:
Output = (ab )' (a + b) = XOR(a, b)
Whose truth table is as follows:
Input 1	Input 2	Output
0	0	0
0	1	1
1	0	1
1	1	0

---
For learning rate = 0.7.
The hidden layer contains two neurons.
For the first neuron, the weights are (-1.36 , -7.65, -7.65)
And its truth table is as follows, which corresponds to the rule,
a'b'
Input 1	Input 2	Output
0	0	1
0	1	0
1	0	0
1	1	0

---
For the second neuron, the weights are ( 3.99, 2.71, 2.71).
And its truth table is as follows, which corresponds to the rule,
ab
Input 1	Input 2	Output
0	0	0
0	1	0
1	0	0
1	1	1

---
The output layer contains one neurons.
For this neuron, the weights are (-2.99, -6.92, -5.58)
And its truth table is as follows, which corresponds to the rule,
a'b'
Input 1	Input 2	Output
0	0	1
0	1	0
1	0	0
1	1	0

---
Conclusion:
The output of XOR is calculated as follows:
Output = (a'b' )' (ab)' = XOR(a, b)
Whose truth table is as follows:
Input 1	Input 2	Output
0	0	0
0	1	1
1	0	1
1	1	0

---
3 Bit Palindrome
For learning rate = 0.6.
The hidden layer contains three neurons.
For the first neuron, the weights are (2.22, 3.93, -0.11, -4.13)
And its truth table is as follows, which corresponds to the rule,
(ac')

---
Input 1	Input 2	Input 3	Output
0	0	0	0
0	0	1	0
0	1	0	0
0	1	1	0
1	0	0	1
1	0	1	0
1	1	0	1
1	1	1	0

---
For the second neuron, the weights are (0.41, 0.67, 0.62, -0.47).
And its truth table is as follows, which corresponds to the rule,
a'bc'+ab'c'+ab
Input 1	Input 2	Input 3	Output
0	0	0	0
0	0	1	0
0	1	0	1
0	1	1	0
1	0	0	1
1	0	1	0
1	1	0	1
1	1	1	1

---
For the third neuron, the weights are (2.41, -4.42, -0.11, 4.18).
And its truth table is as follows, which corresponds to the rule,
a'c
Input 1	Input 2	Input 3	Output
0	0	0	0
0	0	1	1
0	1	0	0
0	1	1	1
1	0	0	0
1	0	1	0
1	1	0	0
1	1	1	0

---
The output layer contains one neurons.
For this neuron, the weights are (-2.45, -5.29, 0.29, -5.24)
And its truth table is as follows, which corresponds to the rule,
a'c'
Input 1	Input 2	Input 3	Output
0	0	0	1
0	0	1	0
0	1	0	1
0	1	1	0
1	0	0	0
1	0	1	0
1	1	0	0
1	1	1	0

---
Conclusion:
The output of Palindrome is calculated as follows:
Output = (ac' )' (a'c)' = Palindrome(a, b, c)
Whose truth table is as follows:
Input 1	Input 2	Input 3	Output
0	0	0	1
0	0	1	0
0	1	0	1
0	1	1	0
1	0	0	0
1	0	1	1
1	1	0	0
1	1	1	1